## Slide 1: BASIC ELECTRONICS (24B11EC111) UNIT-2 Lecture-7 (Clipper Circuits)

## Slide 2: Outline
Content
  Introduction to clippers
  Classifications
  Series clipper
  Parallel clipper
  Biased clipper
  Examples
  Combination clipper
  Summary of clippers
  Reference

## Slide 3: Introduction of clipper
Clippers are networks that employ diodes to “clip” away a portion of an input signal without distorting the remaining part of the applied waveform.
A circuit which use to remove the peak of the wave is called clipper.
Ref 1

## Slide 4: Why clipper used?
The purpose of clippers is to protect a circuit against too high or too low voltages.
A simplest clipper circuit 
Ref 1
Vin

## Slide 5: Classification of clippers
Ref 1
According to non- linear devices used
  Diode clippers and Transistor clippers
According to circuit configuration
  Series clippers and Parallel clippers
According to biasing
  Biased clippers and Unbiased clippers.
According to level of clipping
  Positive clippers, Negative clippers and combination clippers

## Slide 6: Series and Parallel clippers
Ref 1
Series configuration
R
D
V0
Vi
If ,Vi < Vd, diode OFF, V0=0
R
V0
Vi
R.B

## Slide 7: Series…
If, Vi > Vd, diode ON, V0 = Vi -Vd
R
V0
Vi
F.B
+ -
Vd
Where, Vd=0 V (for ideal diode)
Vd=0.7 V (practical diode or silicon diode)
Red line represent Practical diode and Blue line for Ideal diode
Input and output waveform

## Slide 8: Parallel
Where, Vd=0 V (for ideal diode)
Vd=0.7 V (practical diode or silicon diode)
Parallel configuration
R
D
V0
Vi
If ,Vi > Vd, positive half cycle
diode ON, V0=Vd
R
V0
Vi
F.B
+
-
Vd
Ref 1
Where R is extremely small

## Slide 9: Parallel...
R
D
V0
Vi
R.B
If ,Vi < Vd, for negative half cycle
diode OFF V0= -Vi
Input and output waveform
Red line represent Practical diode and Blue line for Ideal diode
Ref 1

## Slide 10: Biased positive clipper
Ref 1
When the input signal voltage is positive.
If Vi < VR, diode is reversed biased and does not conduct. Therefore, Vo = Vi
If Vi > VR, diode is forward biased and thus, Vo= VR+Vd

## Slide 11: Biased negative clipper
When the input signal voltage is negative.
If |Vi |> |VR| , diode is reversed biased and does not conduct. Therefore, Vo = -Vi
If |Vi |< |VR| , diode is forward biased and thus, Vo= - VR-Vd
Vi
V0
VR
Ref 1

## Slide 12: Biased series clippers
R
D
V0
Vi
+ -
VR
R
D
V0=o
+ -
VR
R.B
Fig. 1
Vi<VR + Vd
Fig. 2
i
Ref 1

## Slide 13
R
F.B
V0
Vi>VR + Vd
+ -
VR
Vd
The output voltage by applying KVL
V0=Vi-VR-Vd
Vm
VR + Vd
Diode on
Diode off
Vi
T/2
T
Vm –VR -Vd
Vo
T/2
T
KVL
VR + Vd
diode change the state

## Slide 14: Combination (positive and negative) clipper
When a portion of both positive and negative of each half cycle of the input voltage is to be clipped (or removed), combination clipper is employed.
The circuit for such a clipper is shown in below fig.
Ref 1

## Slide 15: Combination clipper…
During the positive half cycle, the diode D1 is forward biased by the input supply voltage Vi and reverse biased by the reference voltage V1. On the other hand, the diode D2 is reverse biased by both input supply voltage Vi and reference voltage V2
  if Vi<V1, V0=Vi , D1 and D2 off
  If Vi>V1, Vo=V1, D1 on and D2 off
During the negative half cycle, the diode D1 is reverse biased by both input supply voltage Vi and reference voltage V1. On the other hand, the diode D2 is forward biased by the input supply voltage Vi and reverse biased by the reference voltage V2.
  if Vi<V2, V0= -Vi , D1 and D2 off
  If Vi>V2, Vo=V1, D1 off and D2 on
Ref 1

## Slide 16: Summary of clippers
Ref 1

## Slide 18: References
[1] R. Boylestad and L. Nashelsky, ‘Electronic Devices and Circuit Theory’, PHI, 7e, 2001.